## Slide 1: PIRAC Nitriding of a NiTi Shape Memory Alloy: Augmentation of Degradation Resistance
Matthias Debono
Supervised by Dr Ing. Glenn Cassar
Co-supervisor Dr Ing. Joseph Buhagiar
The research work disclosed in this publication is partially funded by the ENDEAVOUR Scholarships Scheme. “The scholarship is part-financed by the European Union – European Social Fund”

## Slide 2: Background
Applications: Cardiovascular stents, orthodontic braces,
minimally invasive surgical devices, Simon’s filter
Advantages
  Shape memory effect,
  Superelasticity
Shortcomings
  High nickel content,
  Poor local corrosion resistance in chloride-containing environments,
  Healing of the passive film is a slow and difficult process
Figure 1: Self-Expanding Nitinol Stent System [1]
[1] Rontis Medical, "Zeus SX," Rontis Medical, [Online]. Available: http://rontismedical.com/zeus-sx/. [Accessed 4 March 2018].
Page 1/4

## Slide 3: Solution by Surface Engineering
Figure 2: A typical PIRAC nitriding setup [2]
NiTi
[2] T. Bonello, J. A.-B. Wilson, J. Housden, E. Y. Gutmanas, I. Gotman, A. Matthews, A. Leyland and G. Cassar, "Evaluating the effects of PIRAC nitrogen-diffusion treatments on the mechanical performance of Ti-6Al-4V alloy," Materials Science and Engineering A, vol. 619, pp. 300-311, 2014.
Nickel-free outermost TiN layer,
Hard and strongly adherent surface coating,
Enhanced wear and corrosion resistance,
Not a line-of-sight process; excellent for complex biomedical devices,
Minimal capital cost
Page 2/4

## Slide 4: Research Contributions
Augmentation of Corrosion Behaviour
  Electrochemical Impedance Spectroscopy
  Potentiodynamic Testing
  Crevice Corrosion Testing
Effects on Mechanical Behaviour
  Superelasticity Compatibility
  Micro-hardness Testing
Assessment of PIRAC Nitrided Nitinol
Page 3/4

## Slide 5: Participation in BIONECA
Sharing of experiences and knowledge with participants working in similar fields;
Offer my support in the development and advancement of biomaterials for the improvement of the quality of life of society;
Gain insight into current research, developments and innovations.
Page 4/4

## Slide 6
Thank you for your kind attention.